## Slide 1
Attacks
Brute-Force Try all possible PIN codes
Shared Secrets Reuse components between deployments
Replay Attack Replay captured communication data
Predictable Keys Key value is 0 due to global variables
Exploiting Weak Validation Designs
  If a post-boot communication message has a fixed checksum for the same message, it can be captured and replayed, allowing the checksum validation to still succeed
  Many teams use pre-boot validation to confirm the authenticity of the AP and components by sending a fixed secret value. However, this value can be intercepted during communication or extracted by malicious firmware, leading to a security breach as the secret is exposed
How to Fix It
  Ensure that the checksum for a message is unique each time, even if the message itself is unchanged
  Use the challenge-response mechanism to authenticate, rather than using a fixed value
    As illustrated in the diagram below, the AP tries to validate the component
  Do not reuse the same secret for different validation processes
  Ensure that any random number used in the validation process is unpredictable to enhance security
Defensive Highlight
Team Cacti
University at Buffalo
Gaoxiang Liu, Zheyuan Ma, Alex Eastman, Xi Tan, MD Armanuzzaman,
Sagar Mohan, Afton Spiegel, and Sai Bhargav Menta
Advised by: Prof. Ziming Zhao and Prof. Hongxin Hu
Encrypted Sensitive Data
  Flags in the boot message and attestation data are encrypted and stored securely
  Only the AP holds the decryption key
  Even if attackers can read a component's flash memory and SRAM, the flags remain secure
Memory Wiping
  After using sensitive data like keys, fill the memory location with zeros to securely erase it
Mitigate Bruce-Force Attack
  Use the Argon2 keyed-hash algorithm for the inputted PIN and Token; this method is intentionally slow
  Introduce a deliberate delay during the checking
  Longer delay after a failed attempt, the delay is still in effective even reseting the board
  A longer delay after a failed PIN or Token attempt, which remains effective even after resetting the board
Mitigate Fault-Injection Attack
  Introduce random delays in hundreds of CPU cycles
  Execute important conditional expression twice, such as authentication and password checking
Offensive Highlight
Design Overview
Secrets | Key1_Public | Key1_Private | Key2_Public | Key2_Private | AEAD Key | Hash Key & Salt
Stored at | AP | Component | Component | AP | AP | AP
Description | Create signature for AP’s message | Validate signature for AP’s message | Create signature for AP’s message | Validate signature for AP’s message | Decrypt the attestation data and boot message | For attestation PIN and replace Token
Attest
The AP signs a component's random number and sends back the signature for validation. After validation, the component sends encrypted attestation data to the AP for decryption.
Boot
The AP verifies each component by having it sign a random number; the components then validate the AP similarly. On successful validation, both the AP and components boot up.
Post-Boot Communication
To ensure message integrity, the sender must sign the message, including the slave device's I2C address and a random number provided by the receiver, allowing the receiver to validate it.
PIN and Token Checking
Store only the Argon2 keyed-hash values of the PIN and Token. Apply the same hashing algorithm to user input and use constant-time comparison to verify hash values.
① Although brute-force is a slow approach, almost half of the PIN extract flags snagged by our team used brute-force. ② The attack boards this year does not support resetting, which serves as a defense mechanism for brute-force attack. Otherwise, we could brute-force more PIN code! ➂ A complex design may not mean a high security, all thanks to the same secrets shared between deployments! ④ Defense points helped us a lot this year! ⑤ Snatched 72 flags during the attack phase, not too shabby!
Fun Facts